## Slide 1: MOSFETs
25CPES102 · ELECTRONIC MATERIALS AND DEVICES
Metal-oxide-semiconductor
field-effect transistors
LECTURE 3
Dr. Zahraa Ismail
Computer Engineering · Academic Year 2025/2026 · Semester One
Figure: Sedra & Smith, Microelectronic Circuits

## Slide 2: Lecture map
LECTURE 3
ELEC1 · Lecture 3 · MOSFETs
1
Structure and operation
how a channel forms; the threshold voltage
2
I–V characteristics
cutoff, triode and saturation
3
MOSFETs in DC circuits
finding the operating point
4
The MOSFET as an amplifier
transconductance, small-signal model
5
The MOSFET as a switch
BY THE END YOU CAN
Explain how vGS creates a channel and how vDS pinches it off
Pick the right region and use its iD equation
Find the DC operating point of a MOSFET circuit
Find gm and the gain of a simple MOSFET amplifier

## Slide 3: Structure and operation
01
The device and its terminals
No gate voltage: no current
The threshold voltage
Tapering and pinch-off
CMOS; n- and p-channel symbols
1
Structure and operation
2
I–V characteristics
3
MOSFETs in DC circuits
4
The MOSFET as an amplifier
5
The MOSFET as a switch

## Slide 4: The n-channel enhancement MOSFET
1 · STRUCTURE AND OPERATION
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
Four terminals: source (S), gate (G), drain (D) and body (B).
A thin oxide (SiO₂) insulates the gate, so the gate draws no current.
The channel region between the n⁺ source and drain has length L and width W.

## Slide 5: With no gate voltage, no current flows
1 · STRUCTURE AND OPERATION
ELEC1 · Lecture 3 · MOSFETs
Figure: web source, via the original lecture slides
Source and drain are n⁺, the body is p-type: two back-to-back pn junctions lie between source and drain.
Whatever the polarity of vDS, one junction is reverse-biased, so iD ≈ 0.
The energy barrier (left) keeps the electrons of the source away from the drain.

## Slide 6: Creating a channel: the threshold voltage
1 · STRUCTURE AND OPERATION
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
A positive vGS pushes holes away from the region under the gate and draws electrons in from the n⁺ source and drain.
Once enough electrons gather, they form an n-type inversion layer: the channel linking source to drain.
DEFINITION
Threshold voltage Vt: the value of vGS at which the channel just forms.

## Slide 7: Increasing vDS: the channel tapers and pinches off
1 · STRUCTURE AND OPERATION
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
Along the channel, the voltage rises from 0 at the source to vDS at the drain.
The gate-to-channel voltage therefore falls from vGS to vGS − vDS: the channel gets shallower toward the drain.
PINCH-OFF
When vDS = vGS − Vt, the channel depth at the drain end falls to almost zero. Increasing vDS further barely changes iD: the current saturates.

## Slide 8: CMOS: NMOS and PMOS on one chip
1 · STRUCTURE AND OPERATION
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
The PMOS transistor is built in an n-well, with p⁺ source and drain.
Thick oxide isolates neighbouring devices. CMOS circuits use both types together.

## Slide 9: Circuit symbols: n-channel and p-channel
1 · STRUCTURE AND OPERATION
ELEC1 · Lecture 3 · MOSFETs
Figure: web source, via the original lecture slides
In these symbols the arrow is on the body: it points in for an n-channel device and out for a p-channel device.
PMOS: holes carry the current and every voltage and current is reversed. It conducts when vGS < Vt, with Vt negative.

## Slide 10: I–V characteristics
02
The iD–vDS family
Saturation: the square law
Triode and saturation equations
Resistor and large-signal models
1
Structure and operation
2
I–V characteristics
3
MOSFETs in DC circuits
4
The MOSFET as an amplifier
5
The MOSFET as a switch

## Slide 11: The iD–vDS family of curves
2 · I–V CHARACTERISTICS
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
Each curve is one value of vGS > Vt.
Left of the dashed line (vDS < vGS − Vt): triode. iD rises with vDS.
Right of it: saturation. iD is set by vGS alone.
For vGS ≤ Vt: cutoff, iD = 0.

## Slide 12: In saturation, iD depends only on vGS
2 · I–V CHARACTERISTICS
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
Measured in saturation, the transfer characteristic is a parabola that starts at vGS = Vt.
i_D = \frac{1}{2}\,k_n^{\prime}\frac{W}{L}\,(v_{GS}-V_t)^2
Doubling (vGS − Vt) quadruples iD: the square law.

## Slide 13: Triode and saturation: one curve, two equations
2 · I–V CHARACTERISTICS
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
TRIODE
vDS < vGS − Vt
i_D = k_n^{\prime}\frac{W}{L}\left[(v_{GS}-V_t)\,v_{DS}-\frac{1}{2}v_{DS}^2\right]
SATURATION
vDS ≥ vGS − Vt
i_D = \frac{1}{2}\,k_n^{\prime}\frac{W}{L}\,(v_{GS}-V_t)^2
Both require vGS > Vt: without a channel, iD = 0 (cutoff).

## Slide 14: Small vDS: a voltage-controlled resistor
2 · I–V CHARACTERISTICS
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
For vDS ≪ 2(vGS − Vt) the vDS² term is negligible:
i_D \approx k_n^{\prime}\frac{W}{L}\,(v_{GS}-V_t)\,v_{DS}
The channel behaves as a resistor whose value vGS sets:
r_{DS} = \left[k_n^{\prime}\frac{W}{L}\,(v_{GS}-V_t)\right]^{-1}
This is the region used when the MOSFET acts as a closed switch (Section 5).

## Slide 15: Large-signal model in saturation
2 · I–V CHARACTERISTICS
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
In saturation the MOSFET acts as a voltage-controlled current source from drain to source.
The gate draws no current: iG = 0.
i_D = \frac{1}{2}\,k_n^{\prime}\frac{W}{L}\,(v_{GS}-V_t)^2

## Slide 16: MOSFETs in DC circuits
03
Assume, solve, check
Example: the drain voltage
The current mirror
1
Structure and operation
2
I–V characteristics
3
MOSFETs in DC circuits
4
The MOSFET as an amplifier
5
The MOSFET as a switch

## Slide 17: DC analysis: assume, solve, check
3 · MOSFETS IN DC CIRCUITS
ELEC1 · Lecture 3 · MOSFETs
1
Assume
a region, usually saturation (and vGS > Vt).
2
Solve
with that region’s iD equation and KVL/KCL. Reject roots that give vGS < Vt.
3
Check
the assumption: saturation needs vDS ≥ vGS − Vt. If it fails, redo it in triode.
The gate draws no current, so gate-bias resistors form an unloaded divider.

## Slide 18: Example: find the drain voltage
3 · MOSFETS IN DC CIRCUITS
ELEC1 · Lecture 3 · MOSFETs
Given Vt = 1 V and k′n(W/L) = 1 mA/V². The gate draws no current.
+VDD = 10 V
RG1 = 10 MΩ
RG2 = 10 MΩ
RD = 6 kΩ
RS = 6 kΩ
VG = 5 V
VS = 3 V
VD = 7 V
1
Gate voltage: the divider is unloaded
V_G = V_{DD}\,\frac{R_{G2}}{R_{G1}+R_{G2}} = 5\ \mathrm{V}
2
Assume saturation, with VGS = VG − IDRS (I in mA, R in kΩ)
I_D = \frac{1}{2}(1)\,(5-6I_D-1)^2
3
Solve the quadratic
18I_D^2-25I_D+8=0\ \Rightarrow\ I_D=0.89\ \text{or}\ 0.5\ \mathrm{mA}
4
ID = 0.89 mA would give VGS = −0.33 V < Vt (no channel): reject.
So ID = 0.5 mA and VGS = 2 V.
5
Drain voltage
V_D = V_{DD} - I_DR_D = 10 - 0.5(6) = 7\ \mathrm{V}
VD = 7 V
✓ VDS = 4 V ≥ VGS − Vt = 1 V: saturation holds.

## Slide 19: The current mirror
3 · MOSFETS IN DC CIRCUITS
ELEC1 · Lecture 3 · MOSFETs
Figure: web source, via the original lecture slides
Q1 is diode-connected (gate tied to drain), so it is in saturation. RSET sets its current IREF, and with it VGS.
Q2 has the same VGS. If it is also in saturation, its current scales with W/L:
\frac{I_O}{I_{REF}} = \frac{(W/L)_2}{(W/L)_1}
Identical transistors copy the current: IO = IREF.

## Slide 20: The MOSFET as an amplifier
04
The load line
Transconductance gm
Small-signal models
Example: gain and input resistance
1
Structure and operation
2
I–V characteristics
3
MOSFETs in DC circuits
4
The MOSFET as an amplifier
5
The MOSFET as a switch

## Slide 21: Amplifier action: the load line
4 · THE MOSFET AS AN AMPLIFIER
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
Figure: web source, via the original lecture slides
v_{DS} = V_{DD} - R_D\,i_D
Bias the MOSFET in saturation, between A and B.
A small change in vGS moves the operating point along the line: a large change in vDS.

## Slide 22: Small-signal operation: the transconductance gm
4 · THE MOSFET AS AN AMPLIFIER
ELEC1 · Lecture 3 · MOSFETs
1
The gate voltage is the bias plus a small signal
v_{GS} = V_{GS} + v_{gs}
2
Substitute into the saturation equation
i_D = \frac{1}{2}k_n^{\prime}\frac{W}{L}(V_{GS}-V_t)^2 + k_n^{\prime}\frac{W}{L}(V_{GS}-V_t)\,v_{gs} + \frac{1}{2}k_n^{\prime}\frac{W}{L}\,v_{gs}^2
3
If vgs ≪ 2(VGS − Vt), the last term is negligible: the signal current is linear in vgs
i_d = g_m v_{gs},\ \ \ \ \ g_m = k_n^{\prime}\frac{W}{L}\,(V_{GS}-V_t)
4
With a drain resistor RD, the voltage gain is
A_v = \frac{v_{ds}}{v_{gs}} = -g_m R_D

## Slide 23: Small-signal equivalent circuits
4 · THE MOSFET AS AN AMPLIFIER
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
Figure: Sedra & Smith, Microelectronic Circuits
The MOSFET as a voltage-controlled current source gmvgs; no current into the gate.
Adding ro = VA/ID models the slight slope of the saturation curves (VA: the Early voltage).

## Slide 24: Example: gain and input resistance
4 · THE MOSFET AS AN AMPLIFIER
ELEC1 · Lecture 3 · MOSFETs
Vt = 1.5 V, k′n(W/L) = 0.25 mA/V², VA = 50 V. Coupling capacitors are short circuits for the signal. Find Av = vo/vi and Rin.
Figure: Sedra & Smith, Microelectronic Circuits
1
DC: no gate current, so VGS = VD (I in mA)
V_D = 15 - 10I_D,\ \ \ \ \ I_D = \frac{1}{2}(0.25)\,(V_D-1.5)^2
ID = 1.06 mA, VGS = VD = 4.4 V
2
Small-signal parameters
g_m = 0.25\,(4.4-1.5) = 0.728\ \mathrm{mA/V},\ \ \ \ \ r_o = \frac{50}{1.06} = 47\ \mathrm{k}\Omega
3
Gain (RG carries negligible signal current)
A_v \approx -g_m\,(R_D\,\|\,R_L\,\|\,r_o) = -0.728\,(4.52) = −3.29\ \mathrm{V/V}
4
Input resistance: RG bridges input and output (Miller effect)
R_{in} = \frac{R_G}{1-A_v} = \frac{10}{4.29} = 2.33\ \mathrm{M}\Omega
Av ≈ −3.3 V/V
Rin = 2.33 MΩ

## Slide 25: The MOSFET as a switch
05
Cutoff: an open switch
Deep triode: a closed switch
1
Structure and operation
2
I–V characteristics
3
MOSFETs in DC circuits
4
The MOSFET as an amplifier
5
The MOSFET as a switch

## Slide 26: The MOSFET as a switch
5 · THE MOSFET AS A SWITCH
ELEC1 · Lecture 3 · MOSFETs
Figure: web source, via the original lecture slides
vGS < Vt: cutoff. The switch is open and iD = 0.
vGS high and vDS small: deep triode. The switch is closed, with a small resistance rDS.
Driving the gate between these two states is the basis of digital logic.

## Slide 27: Summary: three regions of operation
LECTURE 3 · SUMMARY
ELEC1 · Lecture 3 · MOSFETs
REGION
CONDITION
DRAIN CURRENT
Cutoff
vGS ≤ Vt
i_D = 0
Triode
vGS > Vt, vDS < vGS − Vt
i_D = k_n^{\prime}\frac{W}{L}\left[(v_{GS}-V_t)\,v_{DS}-\frac{1}{2}v_{DS}^2\right]
Saturation
vGS > Vt, vDS ≥ vGS − Vt
i_D = \frac{1}{2}\,k_n^{\prime}\frac{W}{L}\,(v_{GS}-V_t)^2
DC problems: assume a region, solve, then check the assumption.
Small signals: gm = k′n(W/L)(VGS − Vt); a common-source stage has Av = −gmRD.

## Slide 28: Thank you
NEXT LECTURE
Lecture 4: Bipolar junction transistors (BJTs)
With thanks to Dr. Sameh Osama Ezzat, who prepared the original material for this lecture.
Figures: Sedra & Smith, Microelectronic Circuits (Oxford University Press); other diagrams from web sources via the original slides.