## Slide 1: MOSFETs
25CPES102 · Electronic Materials and Devices
Metal-oxide-semiconductor
field-effect transistors
Lecture 3
Dr. Zahraa Ismail
Computer Engineering · Academic Year 2025/2026 · Semester One
Figure: Sedra & Smith, Microelectronic Circuits

## Slide 2: Lecture map
LECTURE 3 · MOSFETS
ELEC1 · Lecture 3 · MOSFETs
01
Structure and operation
how a channel forms; the threshold voltage
02
I–V characteristics
cutoff, triode and saturation
03
MOSFETs in DC circuits
finding the operating point
04
The MOSFET as an amplifier
transconductance, small-signal model
05
The MOSFET as a switch
BY THE END YOU CAN
Explain how vGS creates a channel and how vDS pinches it off
Pick the right region and use its iD equation
Find the DC operating point of a MOSFET circuit
2

## Slide 3: I–V characteristics
02
Increasing vDS: pinch-off
Triode and saturation
The iD–vDS family of curves
1 Structure and operation
2 I–V characteristics
3 MOSFETs in DC circuits
4 The MOSFET as an amplifier
5 The MOSFET as a switch

## Slide 4: Creating a channel: the threshold voltage
1 · STRUCTURE AND OPERATION
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
A positive vGS pushes holes away from the region under the gate and draws electrons in from the n⁺ source and drain.
1/3
4

## Slide 5: Creating a channel: the threshold voltage
1 · STRUCTURE AND OPERATION
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
A positive vGS pushes holes away from the region under the gate and draws electrons in from the n⁺ source and drain.
Once enough electrons gather, they form an n-type inversion layer: the channel that links source to drain.
2/3
5

## Slide 6: Creating a channel: the threshold voltage
1 · STRUCTURE AND OPERATION
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
A positive vGS pushes holes away from the region under the gate and draws electrons in from the n⁺ source and drain.
Once enough electrons gather, they form an n-type inversion layer: the channel that links source to drain.
DEFINITION
Threshold voltage Vt: the value of vGS at which the channel just forms.
3/3
6

## Slide 7: Triode and saturation: one curve, two equations
2 · I–V CHARACTERISTICS
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
1/4
7

## Slide 8: Triode and saturation: one curve, two equations
2 · I–V CHARACTERISTICS
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
Triode vDS < vGS − Vt
2/4
8

## Slide 9: Triode and saturation: one curve, two equations
2 · I–V CHARACTERISTICS
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
Triode vDS < vGS − Vt
Saturation vDS ≥ vGS − Vt
3/4
9

## Slide 10: Triode and saturation: one curve, two equations
2 · I–V CHARACTERISTICS
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
Triode vDS < vGS − Vt
Saturation vDS ≥ vGS − Vt
Both require vGS > Vt: without a channel, iD = 0 (cutoff).
4/4
10

## Slide 11: Example: find the drain voltage
3 · MOSFETS IN DC CIRCUITS
ELEC1 · Lecture 3 · MOSFETs
Given Vt = 1 V and k′n(W/L) = 1 mA/V². Assume the gate draws no current.
+VDD = 10 V
RG1 = 10 MΩ
RG2 = 10 MΩ
RD = 6 kΩ
RS = 6 kΩ
1/6
11

## Slide 12: Example: find the drain voltage
3 · MOSFETS IN DC CIRCUITS
ELEC1 · Lecture 3 · MOSFETs
Given Vt = 1 V and k′n(W/L) = 1 mA/V². Assume the gate draws no current.
+VDD = 10 V
RG1 = 10 MΩ
RG2 = 10 MΩ
RD = 6 kΩ
RS = 6 kΩ
VG = 5 V
1
Gate voltage: the divider is unloaded
2/6
12

## Slide 13: Example: find the drain voltage
3 · MOSFETS IN DC CIRCUITS
ELEC1 · Lecture 3 · MOSFETs
Given Vt = 1 V and k′n(W/L) = 1 mA/V². Assume the gate draws no current.
+VDD = 10 V
RG1 = 10 MΩ
RG2 = 10 MΩ
RD = 6 kΩ
RS = 6 kΩ
VG = 5 V
1
Gate voltage: the divider is unloaded
2
Assume saturation, with VGS = VG − IDRS (I in mA, R in kΩ)
3/6
13

## Slide 14: Example: find the drain voltage
3 · MOSFETS IN DC CIRCUITS
ELEC1 · Lecture 3 · MOSFETs
Given Vt = 1 V and k′n(W/L) = 1 mA/V². Assume the gate draws no current.
+VDD = 10 V
RG1 = 10 MΩ
RG2 = 10 MΩ
RD = 6 kΩ
RS = 6 kΩ
VG = 5 V
1
Gate voltage: the divider is unloaded
2
Assume saturation, with VGS = VG − IDRS (I in mA, R in kΩ)
3
Solve the quadratic
4/6
14

## Slide 15: Example: find the drain voltage
3 · MOSFETS IN DC CIRCUITS
ELEC1 · Lecture 3 · MOSFETs
Given Vt = 1 V and k′n(W/L) = 1 mA/V². Assume the gate draws no current.
+VDD = 10 V
RG1 = 10 MΩ
RG2 = 10 MΩ
RD = 6 kΩ
RS = 6 kΩ
VG = 5 V
1
Gate voltage: the divider is unloaded
2
Assume saturation, with VGS = VG − IDRS (I in mA, R in kΩ)
3
Solve the quadratic
4
ID = 0.89 mA would give VGS = −0.33 V < Vt (no channel): reject it. So ID = 0.5 mA, VGS = 2 V.
5/6
15

## Slide 16: Example: find the drain voltage
3 · MOSFETS IN DC CIRCUITS
ELEC1 · Lecture 3 · MOSFETs
Given Vt = 1 V and k′n(W/L) = 1 mA/V². Assume the gate draws no current.
+VDD = 10 V
RG1 = 10 MΩ
RG2 = 10 MΩ
RD = 6 kΩ
RS = 6 kΩ
VG = 5 V
VS = 3 V
VD = 7 V
1
Gate voltage: the divider is unloaded
2
Assume saturation, with VGS = VG − IDRS (I in mA, R in kΩ)
3
Solve the quadratic
4
ID = 0.89 mA would give VGS = −0.33 V < Vt (no channel): reject it. So ID = 0.5 mA, VGS = 2 V.
5
VD = 7 V
✓ Check: VDS = 4 V ≥ VGS − Vt = 1 V, so saturation holds.
6/6
16

## Slide 17: Summary: three regions of operation
LECTURE 3 · SUMMARY
ELEC1 · Lecture 3 · MOSFETs
REGION
CONDITION
DRAIN CURRENT
Cutoff
vGS ≤ Vt
i_D = 0
Triode
vGS > Vt, vDS < vGS − Vt
i_D = k_n^{\prime}\frac{W}{L}\left[(v_{GS}-V_t)\,v_{DS}-\frac{1}{2}v_{DS}^2\right]
Saturation
vGS > Vt, vDS ≥ vGS − Vt
i_D = \frac{1}{2}\,k_n^{\prime}\frac{W}{L}\,(v_{GS}-V_t)^2
In a DC problem: assume a region, solve, then check the assumption.
Current saturates because the channel is pinched off at the drain end.
17