## Slide 1: MOSFETs
25CPES102 · ELECTRONIC MATERIALS AND DEVICES
Metal-oxide-semiconductor
field-effect transistors
LECTURE 3
Dr. Zahraa Ismail
Computer Engineering · Academic Year 2025/2026 · Semester One
Figure: Sedra & Smith, Microelectronic Circuits

## Slide 2: Lecture map
LECTURE 3
ELEC1 · Lecture 3 · MOSFETs
1
Structure and operation
how a channel forms; the threshold voltage
2
I–V characteristics
cutoff, triode and saturation
3
MOSFETs in DC circuits
finding the operating point
4
The MOSFET as an amplifier
transconductance, small-signal model
5
The MOSFET as a switch
BY THE END YOU CAN
Explain how vGS creates a channel and how vDS pinches it off
Pick the right region and use its iD equation
Find the DC operating point of a MOSFET circuit
Find gm and the gain of a simple MOSFET amplifier
2

## Slide 3: Structure and operation
01
The device and its terminals
No gate voltage: no current
The threshold voltage
Tapering and pinch-off
CMOS; n- and p-channel symbols
1
Structure and operation
2
I–V characteristics
3
MOSFETs in DC circuits
4
The MOSFET as an amplifier
5
The MOSFET as a switch

## Slide 4: The n-channel enhancement MOSFET
1 · STRUCTURE AND OPERATION
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
Four terminals: source (S), gate (G), drain (D) and body (B).
A thin oxide (SiO₂) insulates the gate, so the gate draws no current.
The channel region between the n⁺ source and drain has length L and width W.
4

## Slide 5: With no gate voltage, no current flows
1 · STRUCTURE AND OPERATION
ELEC1 · Lecture 3 · MOSFETs
Figure: web source, via the original lecture slides
Source and drain are n⁺, the body is p-type: two back-to-back pn junctions lie between source and drain.
Whatever the polarity of vDS, one junction is reverse-biased, so iD ≈ 0.
The energy barrier (left) keeps the electrons of the source away from the drain.
5

## Slide 6: Creating a channel: the threshold voltage
1 · STRUCTURE AND OPERATION
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
A positive vGS pushes holes away from the region under the gate and draws electrons in from the n⁺ source and drain.
Once enough electrons gather, they form an n-type inversion layer: the channel linking source to drain.
DEFINITION
Threshold voltage Vt: the value of vGS at which the channel just forms.
6

## Slide 7: Increasing vDS: the channel tapers and pinches off
1 · STRUCTURE AND OPERATION
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
Along the channel, the voltage rises from 0 at the source to vDS at the drain.
The gate-to-channel voltage therefore falls from vGS to vGS − vDS: the channel gets shallower toward the drain.
PINCH-OFF
When vDS = vGS − Vt, the channel depth at the drain end falls to almost zero. Increasing vDS further barely changes iD: the current saturates.
7

## Slide 8: CMOS: NMOS and PMOS on one chip
1 · STRUCTURE AND OPERATION
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
The PMOS transistor is built in an n-well, with p⁺ source and drain.
Thick oxide isolates neighbouring devices. CMOS circuits use both types together.
8

## Slide 9: Circuit symbols: n-channel and p-channel
1 · STRUCTURE AND OPERATION
ELEC1 · Lecture 3 · MOSFETs
D
S
B
G
n-channel
D
S
B
G
p-channel
In these symbols the arrow is on the body: it points in for an n-channel device and out for a p-channel device.
PMOS: holes carry the current and every voltage and current is reversed. It conducts when vGS < Vt, with Vt negative.
9

## Slide 10: I–V characteristics
02
The iD–vDS family
Saturation: the square law
Triode and saturation equations
Resistor and large-signal models
1
Structure and operation
2
I–V characteristics
3
MOSFETs in DC circuits
4
The MOSFET as an amplifier
5
The MOSFET as a switch

## Slide 11: The iD–vDS family of curves
2 · I–V CHARACTERISTICS
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
Each curve is one value of vGS > Vt.
Left of the dashed line (vDS < vGS − Vt): triode. iD rises with vDS.
Right of it: saturation. iD is set by vGS alone.
For vGS ≤ Vt: cutoff, iD = 0.
11

## Slide 12: In saturation, iD depends only on vGS
2 · I–V CHARACTERISTICS
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
Measured in saturation, the transfer characteristic is a parabola that starts at vGS = Vt.
i_D = \frac{1}{2}\,k_n^{\prime}\frac{W}{L}\,(v_{GS}-V_t)^2
Doubling (vGS − Vt) quadruples iD: the square law.
12

## Slide 13: Triode and saturation: one curve, two equations
2 · I–V CHARACTERISTICS
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
TRIODE
vDS < vGS − Vt
i_D = k_n^{\prime}\frac{W}{L}\left[(v_{GS}-V_t)\,v_{DS}-\frac{1}{2}v_{DS}^2\right]
SATURATION
vDS ≥ vGS − Vt
i_D = \frac{1}{2}\,k_n^{\prime}\frac{W}{L}\,(v_{GS}-V_t)^2
Both require vGS > Vt: without a channel, iD = 0 (cutoff).
13

## Slide 14: Small vDS: a voltage-controlled resistor
2 · I–V CHARACTERISTICS
ELEC1 · Lecture 3 · MOSFETs
Figure: Sedra & Smith, Microelectronic Circuits
For vDS ≪ 2(vGS − Vt) the vDS² term is negligible:
i_D \approx k_n^{\prime}\frac{W}{L}\,(v_{GS}-V_t)\,v_{DS}
The channel behaves as a resistor whose value vGS sets:
r_{DS} = \left[k_n^{\prime}\frac{W}{L}\,(v_{GS}-V_t)\right]^{-1}
This is the region used when the MOSFET acts as a closed switch (Section 5).
14

## Slide 15: Large-signal model in saturation
2 · I–V CHARACTERISTICS
ELEC1 · Lecture 3 · MOSFETs
G
iG = 0
S
+
vGS
−
D
iD
In saturation the MOSFET acts as a voltage-controlled current source from drain to source.
The gate draws no current: iG = 0.
The drain current is set by vGS alone:
i_D = \frac{1}{2}\,k_n^{\prime}\frac{W}{L}\,(v_{GS}-V_t)^2
15

## Slide 16: MOSFETs in DC circuits
03
Assume, solve, check
Example: the drain voltage
The current mirror
1
Structure and operation
2
I–V characteristics
3
MOSFETs in DC circuits
4
The MOSFET as an amplifier
5
The MOSFET as a switch

## Slide 17: DC analysis: assume, solve, check
3 · MOSFETS IN DC CIRCUITS
ELEC1 · Lecture 3 · MOSFETs
1
Assume
a region, usually saturation (and vGS > Vt).
2
Solve
with that region’s iD equation and KVL/KCL. Reject roots that give vGS < Vt.
3
Check
the assumption: saturation needs vDS ≥ vGS − Vt. If it fails, redo it in triode.
The gate draws no current, so gate-bias resistors form an unloaded divider.
17

## Slide 18: Example 1: find the drain voltage (1 of 2)
3 · MOSFETS IN DC CIRCUITS
ELEC1 · Lecture 3 · MOSFETs
+VDD = 10 V
RG1 = 10 MΩ
RG2 = 10 MΩ
RD = 6 kΩ
RS = 6 kΩ
VG = 5 V
GIVEN
VDD = 10 V
RG1 = RG2 = 10 MΩ
RD = RS = 6 kΩ
Vt = 1 V, k′n(W/L) = 1 mA/V²
Find the drain voltage VD. The MOSFET’s region is not given.
1
Find the gate voltage VG
No current flows into the gate, so RG1 and RG2 form an unloaded voltage divider.
V_G = \textcolor{#1F6FA8}{V_{DD}}\,\frac{\textcolor{#7A3E9D}{R_{G2}}}{\textcolor{#7A3E9D}{R_{G1}}+\textcolor{#7A3E9D}{R_{G2}}} = \textcolor{#1F6FA8}{10}\cdot\frac{\textcolor{#7A3E9D}{10}}{\textcolor{#7A3E9D}{10}+\textcolor{#7A3E9D}{10}} = 5\ \mathrm{V}
2
Assume the MOSFET is in saturation
The region is unknown. Saturation is the usual bias region; we check this assumption at the end.
I_D = \frac{1}{2}\,\textcolor{#B0186B}{k_n^{\prime}\frac{W}{L}}\,(V_{GS}-\textcolor{#B0186B}{V_t})^2
3
Express VGS through the source resistor
ID flows through RS, lifting the source to VS = IDRS. With ID in mA and R in kΩ, the products are in volts.
V_{GS} = V_G - I_D\,\textcolor{#0E7C7B}{R_S} = 5 - \textcolor{#0E7C7B}{6}\,I_D
18

## Slide 19: Example 1: find the drain voltage (2 of 2)
3 · MOSFETS IN DC CIRCUITS
ELEC1 · Lecture 3 · MOSFETs
+VDD = 10 V
RG1 = 10 MΩ
RG2 = 10 MΩ
RD = 6 kΩ
RS = 6 kΩ
VG = 5 V
VS = 3 V
VD = 7 V
GIVEN
VDD = 10 V
RG1 = RG2 = 10 MΩ
RD = RS = 6 kΩ
Vt = 1 V, k′n(W/L) = 1 mA/V²
4
Substitute VGS into the saturation equation and solve
Units: ID in mA. Expanding gives a quadratic with two roots.
I_D = \frac{1}{2}\,(\textcolor{#B0186B}{1})\,(5 - \textcolor{#0E7C7B}{6}I_D - \textcolor{#B0186B}{1})^2
18I_D^2-25I_D+8=0\ \Rightarrow\ I_D = 0.89\ \text{or}\ 0.5\ \mathrm{mA}
5
Keep the physical root
A valid solution must leave VGS > Vt; otherwise there is no channel and no current.
I_D = 0.89:\ \ V_{GS} = 5-6(0.89) = −0.33\ \mathrm{V} < \textcolor{#B0186B}{V_t}\ \ \text{(reject)}
I_D = 0.5:\ \ V_{GS} = 5-6(0.5) = 2\ \mathrm{V} > \textcolor{#B0186B}{V_t}\ \ \text{(keep)}
6
Find the drain (and source) voltage
V_D = \textcolor{#1F6FA8}{V_{DD}} - I_D\,\textcolor{#0E7C7B}{R_D} = \textcolor{#1F6FA8}{10} - 0.5(\textcolor{#0E7C7B}{6}) = 7\ \mathrm{V},\ \ \ \ V_S = I_D\,\textcolor{#0E7C7B}{R_S} = 3\ \mathrm{V}
7
Check the saturation assumption
Saturation needs VDS ≥ VGS − Vt.
V_{DS} = 7-3 = 4\ \mathrm{V}\ \geq\ V_{GS}-\textcolor{#B0186B}{V_t} = 1\ \mathrm{V}
✓ The assumption holds.
VD = 7 V
with ID = 0.5 mA, VGS = 2 V
19

## Slide 20: The current mirror
3 · MOSFETS IN DC CIRCUITS
ELEC1 · Lecture 3 · MOSFETs
VDD
RSET
IREF
IO
Q1
Q2
Q1 is diode-connected (gate tied to drain), so it is in saturation. RSET sets its current IREF, and with it VGS.
Q2 has the same VGS. If it is also in saturation, its current scales with W/L:
\frac{I_O}{I_{REF}} = \frac{(W/L)_2}{(W/L)_1}
Identical transistors copy the current: IO = IREF.
20

## Slide 21: The MOSFET as an amplifier
04
The load line
Transconductance gm
Small-signal models
Example: gain and input resistance
1
Structure and operation
2
I–V characteristics
3
MOSFETs in DC circuits
4
The MOSFET as an amplifier
5
The MOSFET as a switch

## Slide 22: Amplifier action: the load line
4 · THE MOSFET AS AN AMPLIFIER
ELEC1 · Lecture 3 · MOSFETs
VDD
RD
iD
vDS
+
−
vGS
vDS (V)
iD (mA)
vGS = Vt + 1
vGS = Vt + 2
vGS = Vt + 3
vGS = Vt + 4
A
B
load line: iD = (VDD − vDS)/RD
VDD
VDD/RD
v_{DS} = V_{DD} - R_D\,i_D
KVL at the drain: every operating point lies on this line.
Between A (edge of triode) and B (cutoff) the MOSFET is in saturation: bias it there.
A small change in vGS moves the point along the line: a large change in vDS.
Curves computed for k′n(W/L) = 1 mA/V², VDD = 10 V, RD = 1.25 kΩ.
22

## Slide 23: Small-signal operation: the transconductance gm
4 · THE MOSFET AS AN AMPLIFIER
ELEC1 · Lecture 3 · MOSFETs
1
The gate voltage is the bias plus a small signal
v_{GS} = V_{GS} + v_{gs}
2
Substitute into the saturation equation
i_D = \frac{1}{2}k_n^{\prime}\frac{W}{L}(V_{GS}-V_t)^2 + k_n^{\prime}\frac{W}{L}(V_{GS}-V_t)\,v_{gs} + \frac{1}{2}k_n^{\prime}\frac{W}{L}\,v_{gs}^2
3
If vgs ≪ 2(VGS − Vt), the last term is negligible: the signal current is linear in vgs
i_d = g_m v_{gs},\ \ \ \ \ g_m = k_n^{\prime}\frac{W}{L}\,(V_{GS}-V_t)
4
With a drain resistor RD, the voltage gain is
A_v = \frac{v_{ds}}{v_{gs}} = -g_m R_D
23

## Slide 24: Small-signal equivalent circuits
4 · THE MOSFET AS AN AMPLIFIER
ELEC1 · Lecture 3 · MOSFETs
G
S
+
vgs
−
D
gmvgs
G
S
+
vgs
−
D
gmvgs
ro
The MOSFET as a voltage-controlled current source gmvgs; no current into the gate.
Adding ro = VA/ID models the slight slope of the saturation curves (VA: the Early voltage).
24

## Slide 25: Example 2: bias point (1 of 2)
4 · THE MOSFET AS AN AMPLIFIER
ELEC1 · Lecture 3 · MOSFETs
+VDD = 15 V
RD = 10 kΩ
RG = 10 MΩ
+
vi
Rin
RL = 10 kΩ
vo
CC
CC
GIVEN
VDD = 15 V
RG = 10 MΩ
RD = RL = 10 kΩ
Vt = 1.5 V, k′n(W/L) = 0.25 mA/V², VA = 50 V
Find the gain Av = vo/vi and the input resistance Rin. First, the DC bias point.
1
Keep only the DC circuit
Coupling capacitors are open circuits at DC, so vi, RL and the output terminal drop out.
2
Relate VGS to VD
No gate current flows, so there is no drop across RG: VG = VD. With the source grounded, VGS = VDS ≥ VGS − Vt: saturation is guaranteed.
V_{GS} = V_D = \textcolor{#1F6FA8}{15} - \textcolor{#0E7C7B}{10}\,I_D
3
Solve for the bias current (ID in mA)
I_D = \frac{1}{2}\,(\textcolor{#B0186B}{0.25})\,(V_D - \textcolor{#B0186B}{1.5})^2
12.5I_D^2 - 34.75I_D + 22.78 = 0\ \Rightarrow\ I_D = 1.06\ \text{or}\ 1.72\ \mathrm{mA}
ID = 1.72 mA gives VGS = −2.21 V < Vt: reject. So ID = 1.06 mA and VGS = VD = 4.41 V.
25

## Slide 26: Example 2: gain and input resistance (2 of 2)
4 · THE MOSFET AS AN AMPLIFIER
ELEC1 · Lecture 3 · MOSFETs
+VDD = 15 V
RD = 10 kΩ
RG = 10 MΩ
+
vi
Rin
RL = 10 kΩ
vo
CC
CC
GIVEN
VDD = 15 V
RG = 10 MΩ
RD = RL = 10 kΩ
Vt = 1.5 V, k′n(W/L) = 0.25 mA/V², VA = 50 V
4
Small-signal parameters at the bias point
g_m = \textcolor{#B0186B}{k_n^{\prime}\frac{W}{L}}\,(V_{GS}-\textcolor{#B0186B}{V_t}) = \textcolor{#B0186B}{0.25}\,(4.41-\textcolor{#B0186B}{1.5}) = 0.728\ \mathrm{mA/V}
r_o = \frac{\textcolor{#B0186B}{V_A}}{I_D} = \frac{\textcolor{#B0186B}{50}}{1.06} = 47.2\ \mathrm{k}\Omega
5
Find the load seen by the drain
Capacitors are shorts for the signal. RG is so large that its signal current is negligible.
\textcolor{#0E7C7B}{R_D}\,\|\,\textcolor{#0E7C7B}{R_L}\,\|\,r_o = \textcolor{#0E7C7B}{10}\,\|\,\textcolor{#0E7C7B}{10}\,\|\,47.2 = 4.52\ \mathrm{k}\Omega
6
Voltage gain
A_v = \frac{v_o}{v_i} \approx -g_m\,(R_D\,\|\,R_L\,\|\,r_o) = -0.728\times4.52 = −3.29\ \mathrm{V/V}
7
Input resistance (Miller effect)
RG joins input and output. The output swings by Avvi, so the current into RG is (1 − Av)vi/RG: the input sees RG divided by (1 − Av).
R_{in} = \frac{\textcolor{#7A3E9D}{R_G}}{1-A_v} = \frac{\textcolor{#7A3E9D}{10}}{1+3.29} = 2.33\ \mathrm{M}\Omega
Av ≈ −3.3 V/V
Rin = 2.33 MΩ
26

## Slide 27: The MOSFET as a switch
05
Cutoff: an open switch
Deep triode: a closed switch
1
Structure and operation
2
I–V characteristics
3
MOSFETs in DC circuits
4
The MOSFET as an amplifier
5
The MOSFET as a switch

## Slide 28: The MOSFET as a switch
5 · THE MOSFET AS A SWITCH
ELEC1 · Lecture 3 · MOSFETs
VDD
RD
vO
vI
≡
VDD
RD
vO
open: vI < Vt
closed: vI high
vGS < Vt: cutoff. The switch is open and iD = 0.
vGS high and vDS small: deep triode. The switch is closed, with a small resistance rDS.
Driving the gate between these two states is the basis of digital logic.
28

## Slide 29: Summary: three regions of operation
LECTURE 3 · SUMMARY
ELEC1 · Lecture 3 · MOSFETs
REGION
CONDITION
DRAIN CURRENT
Cutoff
vGS ≤ Vt
i_D = 0
Triode
vGS > Vt, vDS < vGS − Vt
i_D = k_n^{\prime}\frac{W}{L}\left[(v_{GS}-V_t)\,v_{DS}-\frac{1}{2}v_{DS}^2\right]
Saturation
vGS > Vt, vDS ≥ vGS − Vt
i_D = \frac{1}{2}\,k_n^{\prime}\frac{W}{L}\,(v_{GS}-V_t)^2
DC problems: assume a region, solve, then check the assumption.
Small signals: gm = k′n(W/L)(VGS − Vt); a common-source stage has Av = −gmRD.
29

## Slide 30: Thank you
NEXT LECTURE
Lecture 4: Bipolar junction transistors (BJTs)
With thanks to Dr. Sameh Osama Ezzat, who prepared the original material for this lecture.
Figures: Sedra & Smith, Microelectronic Circuits (Oxford University Press); other diagrams from web sources via the original slides; circuits and the load-line plot redrawn for this lecture.